Appendix A Precipitation measurements

Introduction

Ⅰ Precipitation gages

Ⅱ Accuracy

Ⅲ Measurements

Introduction

- Measurements of precipitation: precipitation gages, point measurements

- Accuracy: from point to estimate watershed-precipitation

Ⅰ Precipitation

- Nonrecording gages

  - Open cylinder: Table A.1

  - Standard nonrecording precipitation gage: five types (fig. A.1)

- Recording gages

  - Precipitation information: time of occurrence, duration, intensity

  - Weighing-type: (fig. A.2a)

  - Tipping-bucket: (fig. A.2b)

- Storage gages

  - Mountainous areas or remote sites

  - Collector large enough to last for a month, a season, or even a half-year.

Ⅱ Accuracy

- Sources of error

  - Error causes: gage geometry, site exposure, wind effect, evaporation, adhesion, color, inclination, splash, …

  - Random and systematic errors in nature

    - Random: topography, surrounding vegetation, aspect, altitude, human sources

    - Systematic: wind effects, wetting, evaporation, splash, gage inclination,

- Wind effects

  - Raindrop angle:

  - Turbulence: updrafts, downdrafts

- True precipitation

  - Point accuracy

  - Areal representativeness

Ⅲ Measurements

- Gage installation

  - Wind is the most critical factor in precipitation measurements

  - Reducing wind effect

- Improvements

  - Shielded gages: fig. A.3

  - Pit gages: fig. A.4

  - Tilted gages: in mountainous areas

  - Lysimeters: measure changes in weight

  - Wind-speed adjustment: equation A.1-3

  - Spherical gages: face the incoming direction of raindrops (fig. A.5-6)

  - Globoscopic pictures: (fig. A.7)

    - Taking globoscopic pictures above the orifice of a rain gage

    - Obtaining wind speed in eight compass directions at the study site

    - Developing equations to estimate the effect of shelter-belt density on wind speeds and catch error by wind speed in eight directions