Chapter 5 Water distribution

Introduction

5-1 The globe

5-2 The US

5-3 The hydrologic cycle

Introduction

- Nine planets to the Sun (fig. 5.1)

- Earth’s size and right distance from the sun make it able to keep water in the liquid state.

5-1 The globe

      - Saline water (97.4%)

- Definition: more than 1000 mg of dissolved solids per liter or one part per thousand by weight (ppt). Ocean is about 35 ppt.

- Water around the Earth (Table 5.1)

      - Freshwater (2.6%)

- Ice and glaciers: biggest entity of all freshwater (77.2%)

- Water under the ground: unconfined and confined groundwater (fig. 5.2)

- Lakes: most of this surface water is retained in a few large lakes (Table 5.2)

- Rivers: changeable and uncountable numbers of rivers (Table 5.3)

- Atmospheric water: vapor water

5-2 The US (Table 5.4)

  - Rivers

- Five major rivers in US: Mississippi River, Missouri River, Ohio River, St. Lawrence River, and Columbia River (fig. 5.3)

- Discharge is lower than Amazon River due to rainfall (Table 5.5)

  - Lakes

- Five Great Lakes: Superior, Michigan, Huron, Erie, and Ontario (Table 5.6)

- Man-made reservoirs: 2654 reservoirs > 592 km3, 50,000 small reservoirs, 2 million ponds

5-3 The hydrologic cycle (fig. 5.4)

    - The hydrologic processes

- Precipitation: interception by plants and litters

- Evapotranspiration: evaporation and transpiration

- Runoff: infiltration, percolation, groundwater, overland flow

    - The hydrologic budget

- The globe: precipitation (P) - vaporization (V) = runoff (RO) (Table 5.7)

- The US: 72.4% vaporization, 27.6% runoff (fig. 5.5, 5.6)

- Watershed: P – RO – V + ΔS +ΔL = 0; ΔS and ΔL are changes in soil moistures storage and watershed leakage

    - The energy budget

- Rn = Rs – Rr + Ra – Rg;

Rn: net radiation of a location

Rs: incoming solar radiation

Rr: outgoing solar reflection

Ra: incoming atmospheric radiation

Rg: outgoin terrestrial radiation

- Rn = Lh + Sh + Ch (Table 5.8, 5.9)

Lh: latent heat

Sh: sensible heat

Ch: conductive heat