Chapter 12 Research in forest hydrology

Introduction

12-1 Research issues

12-2 Principles of field studies

12-3 Research methods

12-4 Example of calibration and analyses: the Wagon Wheel Gap study

Introduction

- Two of the earliest research studies in forest hydrology were in 1862 precipitation-interception study in Germany and an experimental-watershed study in Czechoslovakia.

3. 441 major experimental watersheds located in US. (fig. 12.1)

12-1 Research issues

- Objectives

  - Cause and effect

    - Hydrologic cycle in forested watersheds

    - Rainfall-runoff relations

    - Require long-term watershed observations over a wide range of environmental conditions

  - Prediction

    - Develop methodology and models for predicting consequences

    - Provide a basis for management, control, and adjustment

  - Management

    - Based on either cause-and-effect or prediction capability

    - Must be evaluated in terms of economic feasibility and environmental integrity

- Subjects

  - Water functions

    - Water provides many functions important to the environment and human society

    - See chapter 2 and chapter 4

  - Forest functions

    - See chapter 7

    - Forest environmental functions

  - Watershed function

    - Collection and storage of precipitation

    - Discharge of surface and groundwater

    - Support of water chemistry and habitat niches

    - Attenuation of nutrients and pollutants

    - Storage of water, nutrients, and sediments

    - Dissipation and transfer of solar radiation

12-2 Principles of field studies

- Measurements are certain degree of error

  - Heterogeneous nature of the study material

  - The accuracy problem of instruments

  - Human factors

- Control

  - All studies require a control or reference standard for assessment of treatment effects

  - Treatment and control watersheds

- Randomness

  - Improves a study’s accuracy by reducing subjectivity and personal preference in conducting the study

  - Establish certain criteria for site selections

- Replication

  - Provides for a more accurate estimate of experimental error

  - Three or four replicas are used to cover sample variations

12-3 Research methods

- Experimental watersheds

  - Paired-watershed approach: two or more watersheds to be gaged for study

    - Watershed selections

      - Must be representative of the region

      - Ensure similarity

      - Size: from 1 ha to 500 ha. Less than 100 ha

    - Calibration methods

      - Install to monitor hydroclimatic conditions (fig. 12.2)

      - Simple linear-regression analysis (equation 12.1- 12.4)

    - Treatment methods

      - Mechanical, prescribed burning, chemical

      - Buffer strip, water quality

    - Duration of calibration and treatment periods

      - Seven or more years (fig. 12.3)

      - Individual runoff events

    - Treatment effects

      - Posttreatment regression vs. pretreatment regression

      - Double mass analysis (fig. 12.4)

    - Criticisms of the approach: see page 289, 9 items

  - Single-watershed approach

    - Calibration period and treatment period

    - Climatic variables: so need longer calibration period

  - Replicated-watershed approach

    - Principles: replication, randomization, and control

    - Ideal watersheds for replication are very difficult to find

- Upstream-downstream approach

  - Selects two sampling sites along a reach for study

  - Studying water quality, habitat quality, and aquatic organisms

- Experimental plots

  - Monitor surface and subsurface runoff (fig. 12.5)

  - Lysimeter: block of soil completely sealed from its surrounding.

  - Size: 0.01 – 0.1 ha

- Regional analysis

  - Streamflow records and climatic observations are available

  - Statistical techniques: correlation coefficients, regressions

- Watershed simulation

  - Time frame of the estimates can be for

    - Single rainfall-runoff event and routing programs

    - Continuous simulation programs

    - Long-term averages

  - Hydrologic conceptualization (fig. 12.6)

  - Hydrologic models: see page 294-295

12-4 Example of calibration and analyses: the Wagon Wheel Gap study

- Objective: testing the effect of forest clearcutting on annual runoff. Control watershed = 90 ha; treatment watershed 81 ha.

- Hydroclimatic data: precipitation and runoff data (Table 12.1)

- The calibration equation: equation 12.10 (Table 12.2)

- Assessment of treatment effects

  - How much effect?

    - Preliminary assessment (Table 12.3)

    - Based on the calibration equation (Table 12.4)

    - Based on the double-mass analysis

  - Is the effect significant?

    - Covariance analysis (fig. 12.7)

    - The paired t-test